产品规格书

XYT-DAC_QSFP+ 转 QSFP+直连高速线缆

产品特点

●支持速率40Gbps

●支持热插拔

● 长度为 0.5,1, 2, 3, 5 m

●低电磁干扰性

●低功耗 < 0.5W

●电源：+3.3V

●与QSFP+MSA兼容

●工作温度: 0~ 70 °C

应用

●存储区域网络，网络连接存储和存储服务器中的高容量I / O

●交换式结构I / O，如超高带宽交换机和路由器

●数据中心布线基础设施

●网络设备之间的高密度连接

标准

●对电子PIN的ESD：与MIL-STD-883E方法3015.7兼容

●符合IEC 61000-4-3标准的RF抗干扰性

●EMI与FCC Part 15 Class B EN55022 Class B兼容

●RoHS符合2002/95 / EC 4.1和4.2 2005/747 / EC

产品描述

QSFP+转QSFP+直连高速线缆是高性能、低成本的QSFP+互联设备。高速线缆符合SFF-8436和SFF-8431规范。它提供低功耗、短距离互连应用。提供40Gb/s的聚合速率。

建议操作条件

| 参数 | 符号 | 最小值 | 典型值 | 最大值 | 单位 |
| --- | --- | --- | --- | --- | --- |
| 贮藏温度 |  | -10 |  | +85 | °C |
| 工作温度 | Tc | 0 |  | 70 | °C |
| 供电电压 | VCC3 | 3.14 | 3.3 | 3.47 | V |
| 功耗 | PD |  |  | 0.02 | W |

电缆连接:

QSFP+ Pin 描述

| Pin | Logic | Symbol | Name/Description | Notes |
| --- | --- | --- | --- | --- |
| 1 |  | GND | Ground | 1 |
| 2 | CML-I | Tx2n | Transmitter Inverted Data Input |  |
| 3 | CML-I | Tx2p | Transmitter Non-Inverted Data Input |  |
| 4 |  | GND | Ground | 1 |
| 5 | CML-I | Tx4n | Transmitter Inverted Data Input |  |
| 6 | CML-I | Tx4p | Transmitter Non-Inverted Data Input |  |
| 7 |  | GND | Ground | 1 |
| 8 | LVTTL-I | ModSelL | Module Select |  |
| 9 | LVTTL-I | ResetL | Module Reset |  |
| 10 |  | Vcc Rx | +3.3V Power Supply Receiver | 2 |
| 11 | LVCMOSI/O | SCL | 2-wire serial interface clock |  |
| 12 | LVCMOSI/O | SDA | 2-wire serial interface data |  |
| 13 |  | GND | Ground | 1 |
| 14 | CML-O | Rx3p | Receiver Non-Inverted Data Output |  |
| 15 | CML-O | Rx3n | Receiver Inverted Data Output |  |
| 16 |  | GND | Ground | 1 |
| 17 | CML-O | Rx1p | Receiver Inverted Data Output |  |
| 18 | CML-O | Rx1n | Receiver Non-Inverted Data Output |  |
| 19 |  | GND | Ground | 1 |
| 20 |  | GND | Ground | 1 |
| 21 | CML-O | Rx2n | Receiver Inverted Data Output |  |
| 22 | CML-O | Rx2p | Receiver Non-Inverted Data Output |  |
| 23 |  | GND | Ground | 1 |
| 24 | CML-O | Rx4n | Receiver Inverted Data Output |  |
| 25 | CML-O | Rx4p | Receiver Non-Inverted Data Output |  |
| 26 |  | GND | Ground | 1 |
| 27 | LVTTL-O | ModPrsL | Module Present |  |
| 28 | LVTTL-O | IntL | Interrupt |  |
| 29 |  | Vcc Tx | +3.3V Power supply transmitter |  |
| 30 |  | Vcc1 | +3.3V Power supply | 2 |
| 31 | LVTTL-I | LPMode | Low Power Mode |  |
| 32 |  | GND | Ground | 1 |
| 33 | CML-I | Tx3p | Transmitter Non-Inverted Data Input |  |
| 34 | CML-I | Tx3n | Transmitter Inverted Data Input |  |
| 35 |  | GND | Ground | 1 |
| 36 | CML-I | Tx1p | Transmitter Non-Inverted Data Input |  |
| 37 | CML-I | Tx1n | Transmitter Inverted Data Input |  |
| 38 |  | GND | Ground | 1 |

注意:

1：GND是QSFP+模块通用的信号和电源（电源）的符号。所有在QSFP+模块内都是常见的，除非另有说明，所有模块电压都参照此电位。将这些直接连接到主机板信号公共接地平面。

2：VCC RX，VCCC 1和VCC TX是接收器和发射器电源，并应同时应用。VCC RX VCC1和VCC TX可以在内部连接-在QSFP+模块模块中的任何组合。连接器引脚分别额定为500毫安的最大电流。

高速线缆QSFP+主机板示意图

产品尺寸：

订购信息及相关产品

| Part | 描述 |
| --- | --- |
| XYT-DAC_SFP+ to SFP+-CNM1 | QSFP+ 转 QSFP+ 直连高速线缆, 1m (26AWG),0ºC ~ +70ºC |
| XYT-DAC_SFP+ to SFP+-CNM3 | QSFP+ 转 QSFP+ 直连高速线缆, 3m (26AWG),0ºC ~ +70ºC |
| XYT-DAC_SFP+ to SFP+-CNM5 | QSFP+ 转 QSFP+ 直连高速线缆, 5m (26AWG),0ºC ~ +70ºC |