产品规格书

40G QSFP+ 转 4x10G SFP+ 直连高速线缆

产品特点

●符合SFF-8436和SFF-8431

●支持速率：1 Gbps - 10.3125 Gbps（每个信道）

●符合SFP MSA和SFF-8472

●最大总数据速率：41.25 Gbps（4×103125Gb/s）

● 线缆长度可达5m（被动限制）

●高密度QSFP 38引脚和4X SFP 20引脚连接器

●符合RoHS标准

●电源：+3.3V

●操作温度：

商用：0°C至+70°C

应用

●40G QSFP+ to 4×10SFP+

●10G/40G以太网

●无限带宽SDR、DDR、QDR

●开关、路由器和HBAs

●数据中心

●光纤通道

标准符合性QSFP+

●SFF-8436  ●QDR 无限带宽  ●QSFP+ MSA

产品描述

QSFP+到4x SFP+无源电缆组件对于SFP+和QSFP+设备互连是高性能、低成本的。混合电缆（直连高速线缆）符合SFF-8436和SFF-8431规范。它提供低功耗、短距离互连应用。电缆每个分支通道能够以10Gb/s的速率传输数据，提供40Gb/s的聚合速率。

建议操作条件

| 参数 | 符号 | 最低 | 典型 | 最高 | 单位 |
| --- | --- | --- | --- | --- | --- |
| 贮藏温度 |  | -10 |  | +85 | °C |
| 工作温度 | Tc | 0 |  | 70 | °C |
| 供电电压 | VCC3 | 3.14 | 3.3 | 3.47 | V |
| 功耗 | PD |  |  | 0.02 | W |

QSFP+ Pin 描述

| Pin | Logic | Symbol | Name/Description | Notes |
| --- | --- | --- | --- | --- |
| 1 |  | GND | Ground | 1 |
| 2 | CML-I | Tx2n | Transmitter Inverted Data Input |  |
| 3 | CML-I | Tx2p | Transmitter Non-Inverted Data Input |  |
| 4 |  | GND | Ground | 1 |
| 5 | CML-I | Tx4n | Transmitter Inverted Data Input |  |
| 6 | CML-I | Tx4p | Transmitter Non-Inverted Data Input |  |
| 7 |  | GND | Ground | 1 |
| 8 | LVTTL-I | ModSelL | Module Select |  |
| 9 | LVTTL-I | ResetL | Module Reset |  |
| 10 |  | Vcc Rx | +3.3V Power Supply Receiver | 2 |
| 11 | LVCMOSI/O | SCL | 2-wire serial interface clock |  |
| 12 | LVCMOSI/O | SDA | 2-wire serial interface data |  |
| 13 |  | GND | Ground | 1 |
| 14 | CML-O | Rx3p | Receiver Non-Inverted Data Output |  |
| 15 | CML-O | Rx3n | Receiver Inverted Data Output |  |
| 16 |  | GND | Ground | 1 |
| 17 | CML-O | Rx1p | Receiver Inverted Data Output |  |
| 18 | CML-O | Rx1n | Receiver Non-Inverted Data Output |  |
| 19 |  | GND | Ground | 1 |
| 20 |  | GND | Ground | 1 |
| 21 | CML-O | Rx2n | Receiver Inverted Data Output |  |
| 22 | CML-O | Rx2p | Receiver Non-Inverted Data Output |  |
| 23 |  | GND | Ground | 1 |
| 24 | CML-O | Rx4n | Receiver Inverted Data Output |  |
| 25 | CML-O | Rx4p | Receiver Non-Inverted Data Output |  |
| 26 |  | GND | Ground | 1 |
| 27 | LVTTL-O | ModPrsL | Module Present |  |
| 28 | LVTTL-O | IntL | Interrupt |  |
| 29 |  | Vcc Tx | +3.3V Power supply transmitter |  |
| 30 |  | Vcc1 | +3.3V Power supply | 2 |
| 31 | LVTTL-I | LPMode | Low Power Mode |  |
| 32 |  | GND | Ground | 1 |
| 33 | CML-I | Tx3p | Transmitter Non-Inverted Data Input |  |
| 34 | CML-I | Tx3n | Transmitter Inverted Data Input |  |
| 35 |  | GND | Ground | 1 |
| 36 | CML-I | Tx1p | Transmitter Non-Inverted Data Input |  |
| 37 | CML-I | Tx1n | Transmitter Inverted Data Input |  |
| 38 |  | GND | Ground | 1 |

注意:

1：GND是QSFP+模块通用的信号和电源（电源）的符号。所有在QSFP+模块内都是常见的，除非另有说明，所有模块电压都参照此电位。将这些直接连接到主机板信号公共接地平面。

2：VCC RX，VCCC 1和VCC TX是接收器和发射器电源，并应同时应用。VCC RX VCC1和VCC TX可以在内部连接-在QSFP+模块模块中的任何组合。连接器引脚分别额定为500毫安的最大电流。

SFP+ Pin 描述

| PIN | 逻辑 | 符号 | 描述 | Notes |
| --- | --- | --- | --- | --- |
| 1 |  | VeeT | Tx ground |  |
| 2 | LV-TTL-O | Tx Fault | N/A | 1 |
| 3 | LV-TTL-I | Tx Disable | Transmitter Disable | 2 |
| 4 | LV-TTL-I/O | SDA | Tow Wire Serial Data |  |
| 5 | LV-TTL-I | SCL | Tow Wire Serial Clock |  |
| 6 |  | MOD-DEF0 | Module present, connect to VeeT |  |
| 7 | LV-TTL-I | RS0 | N/A | 1 |
| 8 | LV-TTL-O | LOS | LOS of Signal | 2 |
| 9 | LV-TTL-I | N/A | N/A | 1 |
| 10 |  | VeeR | Rx ground |  |
| 11 |  | VeeR | Rx ground |  |
| 12 | CML-O | RD- | Reciever Data Inverted |  |
| 13 | CML-O | RD+ | Reciever Data Non-Inverted |  |
| 14 |  | VeeR | Rx ground |  |
| 15 |  | VccR | Rx power supply |  |
| 16 |  | VccT | Tx power supply |  |
| 17 |  | VeeT | Tx ground |  |
| 18 | CML-I | TD+ | Transmitter Data Non-Inverted |  |
| 19 | CML-I | TD- | Transmitter Data Inverted |  |
| 20 |  | VeeT | Transmitter Ground |  |

注意:

1. 在SFP+铜脉冲下的信号不支持30K欧姆电阻。

2. 无源电缆组件不支持 LOS 和 TX_DIS

产品尺寸

订购信息及相关产品

| Part | Description |
| --- | --- |
| XYT-DAC_QSFP+ 40G-CNM1 | QSFP+ 转 4X SFP+ 直连高速线缆, 1m (30AWG),0ºC ~ +70ºC |
| XYT-DAC_QSFP+ 40G-CNM3 | QSFP+ 转 4X SFP+ 直连高速线缆, 3m (30AWG),0ºC ~ +70ºC |
| XYT-DAC_QSFP+ 40G-CNM5 | QSFP+ 转 4X SFP+ 直连高速线缆, 5m (28AWG),0ºC ~ +70ºC |